## Slide 1
Team LOGO/NAME
CANSAT configuration overview
Configuration — Cutaway (top to bottom)
GNSS antenna + Top cap
Primary drogue (passive, drag)
Steerable main (GPS) @600m
Momentum wheel (gyro stab.)
Avionics + clean-air sensors
Particulate bay (SPS30, ducted)
Heated-gas bay (MQ135/MiCS/UV)
Comms (XBee + NavIC)
Power: 18650, 95 dB beacon + LED
Bottom cap + bumper
Mission: Profile the vertical pollution column (PM, NO2/CO, CO2, NH3, VOC, UV) of the
atmosphere during descent — an urban air-quality & wildfire-smoke mapping CANSAT, on a fully
compliant two-stage parachute + momentum-wheel platform.
~710 g
Total mass (limit 1000 g)
148 x 390 mm
Envelope (max 150 x 400)
1000 m
Deploy altitude
20 -> 1-3 m/s
Drogue -> main descent
Major Components
• Structure: fiberglass/epoxy shell + PLA bulkheads
• Avionics: ESP32 on custom 2-layer PCB
• Descent: drogue + GPS-steered main + wheel
• Comms: XBee Pro S2C + Yagi GS
• Payload: 6-sensor suite + full-flight cam
• Nav: NavIC + targeted landing

## Slide 2
Team LOGO/NAME
Design of subsystems including ground systems
MECHANICAL & STRUCTURE
• Shell: vacuum-bagged E-Glass/epoxy sandwich — RF-transparent (carbon prohibited).
• Bulkheads: 7 PLA+ rings screwed to shell; all PCBs hard-mounted on M3 standoffs.
• Loads: designed for 15 G sustained + 30 G shock (vibration + drop verified).
• Thermal: heated-gas bay isolated from precision baro/CO2 sensors.
• Airflow: ducted inlet/outlet for PM sensor; mesh-screened gas vents.
• Recovery aid: fluorescent orange body + Indian flag + tri-lingual labels + 95 dB beacon.
DESCENT, STABILISATION & TARGETED LANDING
Stage 1 — Drogue (passive)
~20 cm; drag-deploys at ejection; pre-tied to body, NO mechanism; ~20 m/s.
Stage 2 — GPS-guided steerable main
~2.0 m cruciform; release @600 m; 1-3 m/s; 2 winch servos steer to launch pad.
Mechanical gyro — Momentum wheel
Brass wheel on yaw axis, coreless motor, 6-10k RPM; Hall RPM telemetered.
Sequence:
Eject 1000m
>
Drogue 20 m/s
>
Steer @600m
>
Flare + land

## Slide 3
Team LOGO/NAME
Design of subsystems including ground systems
SENSOR & PAYLOAD SUBSYSTEM
Measures | Sensor | Role
Altitude/Pressure/Temp | BMP390 (I2C) | Mandatory — precision altimeter
Orientation/Accel | BNO055 (I2C) | Mandatory — on-chip fusion
Gyro spin rate | A3144 Hall | Mandatory — wheel RPM (field 14)
Position | NavIC GNSS | Mandatory + NavIC bonus
Power status | Divider->ADC | Mandatory — bus voltage
VOC/humidity | BME688 (I2C) | Air-quality baseline / smog
NO2 + CO | MiCS-4514 | Vehicle-exhaust tracer
PM1.0/2.5/10 | SPS30 (I2C) | Haze, soot, wildfire ash
CO2 | SCD41 (I2C) | Combustion / greenhouse
NH3 + benzene | MQ-135 | Industrial / agri off-gassing
UV irradiance | GUVA-S12SD | UV vs altitude
UTC time / logging | DS3231 RTC | Battery-backed clock + SD timestamps
Imaging (opt iii) | Action camera | Full-flight video to own microSD
COMM & DATA HANDLING
• Radio: XBee Pro S2C, 2.4 GHz, point-to-point (no broadcast); PANID = team no.
• Onboard antenna: 1/4-wave whip along body axis (omnidirectional).
• Ground antenna: Yagi-Uda (10-14 dBi) on tripod, polarization-aligned.
• Processor: ESP32 (240 MHz); boot < 2 s.
• Backup: MicroSD logs identical CSV on link loss.
• Clock: mission time persisted to flash — survives reset.
• Format: ASCII CSV + carriage return, >=1 Hz.

## Slide 4
Team LOGO/NAME
Components and hardware realization plan
BILL OF MATERIALS (summary)
Category | Rs. | Notes
Core electronics | 13,720 | ESP32, BMP390, BNO055, NavIC, XBee, SD, power
Atmospheric payload | 10,050 | BME688, MiCS-4514, SPS30, SCD41, MQ-135, UV
Mechanical + structure | 11,728 | Wheel, parachutes, fiberglass, PLA, layup
Contingency (15%) | 5,325 | Spares + testing consumables
TOTAL BUILD | 40,823 | Within Rs. 1,00,000 cap (41%)
FABRICATION & REALIZATION
• 3D-print mandrel -> wet layup E-Glass + foam -> vacuum cure -> trim, drill vents
• Custom 2-layer PCB (JLCPCB) -> solder + bench-test before mounting
• Machine brass wheel; assemble on bearings; balance
• Bottom-up bay integration; fit-check at each stage
PROCUREMENT & MADE-IN-INDIA
• Long-lead first: order SPS30 / SCD41 / MiCS early (import lead times).
• Burn-in: start MQ-135 / MiCS 24-48 h on arrival.
• Made-in-India: structure, PCB, battery, mechanics India-sourced for weightage.
• Tradeoff: payload sensors are imports (science-bonus tradeoff).

## Slide 5
Team LOGO/NAME
Tests undertaken and results
TEST MATRIX (results filled as tests complete)
Test | Method | Pass Criteria | Status
Sensor / payload bench | Power up; read all 11 sensors 10 min | Valid data; no bus errors | [ fill ]
Gas calibration | Burn-in 24-48h; known-source exposure | Repeatable response curves | [ fill ]
PM airflow | Smoke source via ducting | PM2.5 rises; stable fan flow | [ fill ]
Thermal isolation | Run heaters; watch baro/CO2 temp | Precision drift < 1 C | [ fill ]
Power (heater-managed) | 2h pad + warm-up + flight load | Endurance met on 1x 18650 | [ fill ]
Drop test | 2 m onto mat on chute cord | No damage; TM continues | [ fill ]
Vibration test | 60 s launch-profile shake | No detachment (15G/30G) | [ fill ]
Parachute deploy | Drogue drag x5; main servo x10 | Reliable; no entanglement | [ fill ]
Gyro wheel | Spin-up + Hall RPM; tilt body | Stable RPM; attitude stiffness | [ fill ]
Full mission sim | SIM altitude profile via GS | All 8 states; full CSV | [ fill ]
Comm range | TX from 1.5 km LOS | >95% packets received | [ fill ]

## Slide 6
Team LOGO/NAME
CANSAT/Model Rocket mission control software and ground systems
FLIGHT SOFTWARE STATE MACHINE (per Rule 6.2)
0 BOOT
>
1 TEST_MODE
>
2 LAUNCH_PAD
>
3 ASCENT
4 ROCKET_DEPLOY
>
5 DESCENT
>
6 AEROBREAK_REL
>
7 IMPACT
Mission time + state persisted to flash (NVS) — restored on reset so the clock never restarts.
TELEMETRY (16 mandatory + payload)
• ID, time, packet#, altitude, pressure, temp, voltage
• GNSS time/lat/lon/alt/sats, accel, gyro-RPM, state
• Appended payload: PM1/2.5/10, NO2, CO, CO2, NH3, VOC, UV
• Guidance + RTC: bearing, dist-to-pad, heading, UTC time
• File: Flight_<TEAM_ID>.csv, headers, >=1 Hz
GROUND STATION
• Software: Python (PyQt5 + pyqtgraph), all fields plotted in SI
• Commands: START/STOP TX, CAL, SET_WAYPOINT, HEATER, SIM
• Dashboard: live pollutant-vs-altitude profiles + GNSS map
• Hardware: laptop >=2 h + XBee + Yagi on tripod

## Slide 7
Team LOGO/NAME
Realization and readiness plan including Quality control
DEVELOPMENT MILESTONES
Register
by 30 Apr
>
PDR
May
>
Procure+Build
Jun-Jul
>
CDR
31 Jul
>
Test+Integrate
Aug-Sep
>
FRR
by 15 Oct
>
Launch
Oct-Nov
QUALITY CONTROL
• Every subsystem tested before integration
• Environmental tests: drop, vibration, thermal
• Full mission simulation before FRR
• Sensor calibration curves documented
• Version-controlled firmware + change log
COMPLIANCE
42 / 42
requirements compliant by design
• All mandatory rules met
• +4 optional objectives (i,ii,iii,iv)
• NavIC + Made-in-India weightage
READINESS STATEMENT
The design is mature, fully compliant, and
buildable within budget and schedule. It
adds a distinctive atmospheric pollution
payload, video + targeted landing on a
two-stage parachute + momentum-wheel
platform — ready to proceed to CDR.